## Slide 1
Rotating Detonation Engine Activities – T(H)RUST
Alessandro Montanari, Marco Grossi, Alex Falco, Francesco Nasuti

## Slide 2
HEM modeling for subcritical flows in liquid rocket engine cooling systems
2/17
Research Roads
Group Overview
“Newborn” RDE activity
About 1.5 years of active R&D on Rotating Detonation Engines
Numerical focus
URANS / low-order in-house modelling of RDEs, oriented to industrially-relevant challenges
International network
Joint RDE activities with BEFAST Lab (NC State, Prof. James Braun), RMIT (Quentin Michalski) and ISAE-ENSMA (Prof. Marc Belleonue)
HYPERDE
A hybrid-dimensional CFD modelling framework that solves chamber, injector, plenum and expansion with a consistent low-order formulation
Open research lines
Study of hot topics of the RDE community: refill region, supersonic bladeless turbines, disk RDEs, nozzle design, heat flux

## Slide 3
HEM modeling for subcritical flows in liquid rocket engine cooling systems
3/18
Code Development and Capabilities
HYPERDE (HYbrid-dimensional PERformance-predictive numerical framework for Rotating Detonation Engines)
Chamber
3D / Q2D (unwrapped)
Fully 3D or “unwrapped” Q2D URANS/Eulerian solver for the annular chamber
Plenum
3D / Q2D
Fully 3D (2D for unwrapped) solver for the upstream feed plenum
Injectors
3D / Q2D / Eulerian quasi-1D
Quasi-1D solver captures the longitudinal transient response in strongly injector-coupled cases
Expansion System
3D URANS / Q2D chamber coupling
3D URANS solver coupled with the chamber 3D/Q2D exhaust (choked and unchoked outflows)
Rationale: each engine subsystem is solved at its most informative dimensionality

## Slide 4
HEM modeling for subcritical flows in liquid rocket engine cooling systems
4/18
Code Development and Capabilities
General features of the solvers’ suite
• Finite volume method
• II order in space, up to III order in time
• Several turbulence models (easily extendable; strong modularity)
• Tabulated thermo properties, thermally perfect gas
• Flexible pre-processing tool, full integration with .yaml chemical datasets
• Strong CPU parallelization (OpenMP + MPI)
• Lots of degrees of freedom on numerics: Riemann solvers, integrated quantities, stiff chemical ODE solver, …
+
• Interface with other in-house solvers (solid, multiphase, real-fluid)

## Slide 5
HEM modeling for subcritical flows in liquid rocket engine cooling systems
5/18
Code Development and Capabilities
Q2D solver — innovation w.r.t. recent literature
• Rigorous treatment of diffusive fluxes and generic RANS equations
• General derivation with z = z(x,y) — valid for generic width variations
• Adaptation to CFD of the non-isentropic BFS boundary condition [1]
[1] Fievisohn & Yu, “Steady-state analysis of RDE flowfields with the method of characteristics,” J. Propulsion and Power 33(1), 89–99, 2017.

## Slide 6
HEM modeling for subcritical flows in liquid rocket engine cooling systems
6/18
Code Development and Capabilities
V&V
• Validation against 1D ZND H2/Air detonation from SDT

## Slide 7
HEM modeling for subcritical flows in liquid rocket engine cooling systems
7/18
Code Development and Capabilities
V&V
• Validation against “unwrapped” literature test cases [2]
[2] D. Schwer and K. Kailasanath, “Feedback into mixture plenums in rotating detonation engines,” 50th AIAA Aerospace Sciences Meeting, 2012.

## Slide 8
HEM modeling for subcritical flows in liquid rocket engine cooling systems
8/18
Code Development and Capabilities
V&V
• Extensive assessment of HYPERDE features (Q2D source terms, Q1D injectors-chamber, Q2D-3D connection)
AR = 0.4

## Slide 9
HEM modeling for subcritical flows in liquid rocket engine cooling systems
9/18
Code Development and Capabilities
V&V
• Extensive assessment of HYPERDE features (Q2D source terms, Q1D injectors-chamber, Q2D-3D connection)

## Slide 10
HEM modeling for subcritical flows in liquid rocket engine cooling systems
10/18
Code Development and Capabilities
V&V
• Extensive assessment of HYPERDE features (Q2D source terms, Q1D injectors-chamber, Q2D-3D connection)

## Slide 11
HEM modeling for subcritical flows in liquid rocket engine cooling systems
11/18
Characterization of Refill Region Dynamics (with RMIT and NCSU)
How does the geometry affect the refill region expansion process?
What happens if/when expansion yields supersonic Mach number in the layer?
Can the process be modelled?
How does the overall phenomenology impact the stagnation pressure losses?
Understanding physics of RDE refill regions with diverging inlets
Introduced to mitigate separation losses associated with backward-facing steps
Experimental and numerical evidence instead reports degraded overall performance
Inlet extension added for supersonic cases

## Slide 12
HEM modeling for subcritical flows in liquid rocket engine cooling systems
12/18
Characterization of Refill Region Dynamics
Pressure flow field comparison for different inlet expansion ratio
Small amounts of expansion yield partially supersonic refill areas
Supersonic area and loss growth with increasing inlet expansion ratio
For some of the inlet line becomes fully supersonic (and negative PG)!
2D,
Inlet line
premixed

## Slide 13
HEM modeling for subcritical flows in liquid rocket engine cooling systems
13/18
Characterization of Refill Region Dynamics

## Slide 14
HEM modeling for subcritical flows in liquid rocket engine cooling systems
14/18
Supersonic Bladeless Turbines (with NCSU)
CFD based design of NCSU supersonic wind tunnel
Capability up to Mach 4 for steady non-reactive flow
Swappable nozzle and second-throat diffuser system allowing for low feed pressure
Numerical analysis of phenomenology and working principle of bladeless turbines

## Slide 15
HEM modeling for subcritical flows in liquid rocket engine cooling systems
15/18
Supersonic Bladeless Turbines (with NCSU)
CFD based design of NCSU supersonic wind tunnel
Capability up to Mach 4 for steady non-reactive flow
Swappable nozzle and second-throat diffuser system allowing for low feed pressure
Numerical analysis of phenomenology and working principle of bladeless turbines
p0 = 3 bar
p0 = 4 bar

## Slide 16
HEM modeling for subcritical flows in liquid rocket engine cooling systems
16/18
Supersonic Bladeless Turbines (with NCSU)
Ongoing
Bladeless turbine shape optimization
CFD analysis and design of ejector-diffuser system for RDE testing

## Slide 17
HEM modeling for subcritical flows in liquid rocket engine cooling systems
17/18
Disk RDEs (with RMIT and ISAE-ENSMA)
Collaboration with PPRIME lab
CFD lead on design and analysis of disk RDEs operating with H2/Air
3D URANS (or Euler)
Q2D URANS (or Euler)

## Slide 18
HEM modeling for subcritical flows in liquid rocket engine cooling systems
18/18
Nozzle Design for RDEs
• Fully non-isentropic three-waves 2D / 2D-axisymmetric MoC solver developed as an in-house API
• Primary application: nozzle design for ideal, TIC and optimized configurations
• Implemented families: ideal (bell, plug, shrouded plug), Rao (optimal bell and plug) and Veen (optimal shrouded plug)
Open questions (and possible research paths)
• Separation dynamics/topology in plug / shrouded plug (effect of rotating oblique shock on incipient separation [3])
• Does an “optimal” profile exist for an RDE exhaust?
• CFD exploration of the theoretical findings in [4]
Optimized shrouded plug
[3] A. J. Harroun, S. D. Heister, J. H. Ruf, “Computational and experimental study of nozzle performance for rotating detonation rocket engines,” J. Propulsion and Power 37(5), 660–673, 2021.
[4] D. P. Stechmann, S. D. Heister, A. J. Harroun, “Rotating detonation engine performance model for rocket applications,” J. Spacecraft and Rockets 56(3), 887–898, 2019.